## Slide 1
Fire Rated interior Doors
Rafal Madej & Kylie Fletcher

## Slide 2: Reason for Certification
Many houses have at least 1 fire rated door
Interior door quotes had to be divided between Glenview Doors and companies such as Trustile that had the Fire Rating Certification
That created a lot of confusion between dealers and customers specifically when designs and finishes had to match
Timing / delivery issues

## Slide 3: Testing Lab: QAI Laboratories
Founded in 1995
Independent third-party Testing Inspection and Certification Organization
Located in USA and Canada
Fire Door Listing Program - https://qai.org/directory/home- factories-inc-dba-bmd-manufacturing/
Listing number F496

## Slide 4: Testing Standards
The Fire Test of Door Assemblies can be used for neutral or negative pressure tests
Standard for Positive Fire Pressure Test of Door
Assemblies evaluates a door’s
ability to retain its assembly during a positive pressure test.
The Standard Methods of Fire Tests of Door Assemblies can be used for either a positive or neutral pressure test.
The requirements for CAN/ULC S104 certification can be found throughout the National Building Code of Canada for various types of door and frame assemblies
The IBC (International Building Code) references: UL 10B, UL 10C and NFPA 252
The NBC (National Building Code of Canada) references: CAN/ULCS104

## Slide 5: Technical: Doors
Modern Design
  Flush Panel Doors
  Single Swing
  Maximum slab dimensions 42” x 96”
  Minimum slabs thickness 44mm (1-3/4”)
Latching
  UL listed single point lockset hardware approved for use with 20-minute wood type doors
    Tubular
    Mortise
    Mortise Lock with 8mm pin handle, to match Euro style handles

## Slide 6: Doors: Grooving
V-groove A & B
Kerf Cut C
Metal Inlays max 1/16” deep and 13/16” wide

## Slide 7: Doors: Hinges, Door Closers & Door Bottoms
Hinges
  per NFPA 80, Table 6.4.3.1.
  Pol-Soft Estetic 150
  Simonswerk Tectus 340 3D
Door closer
  Mortised closers of maximum size 19-11/16” x 2-5/16" x 1-3/8” (DormakabaITS 9625)
  Surface mounted door closers.

## Slide 8: Technical: Frames
Material: Solid Wood (Solid beach wood or equivalent wood species of the same or greater specific gravity)
Minimum frame depth: 4.5 in. (114 mm)
Maximum frame depth: Equivalent to wall thickness
Minimum frame leg thickness: 2 in. (50.8 mm)
Rabbet size: 1-5/16in. (34 mm)
Q-lon weatherstrip

## Slide 9: Training Tools
Addition of slides to training and sales presentations
Battle cards for how to sell against competitors
One-pager selling sheet for team
Glenview Doors and all other websites to be updated with appropriate content
Kylie to create training schedule for sales teams as needed

## Slide 10
Thank You