## Slide 1: Interior Steel and Glass
Product Line Overview

## Slide 2: Types of Available Units
Standard Swing (single and double)
Pivot
Fixed
Pocket
Barn
Sliding
Variafold

## Slide 3: Quick Facts
Steel Construction with Powder Coated Finish and Zinc Underlayer
Door/fixed slabs are 1-5/8” thick, units (with frame) are 1-7/8” thick
Designed to be installed into FINISHED openings
  Determining unit size: take dimensions of FINISHED opening and subtract 3/8” from width and ¼” from height
  If customer provides desired slab dimensions, add 1-7/8” to the width and 1-3/8” to the height to generate unit size dimensions
Swing and fixed units installed with screws through the frame
Pocket/Sliding/Barn/Variafold units mounted on tracks

## Slide 4: Standard Swing
Single and double door configurations
Sidelights and transoms available
Max width per panel: 48”
Max height per panel: 108”

## Slide 5: Standard Swing – In-stock
Available as single and double doors
  System 20 – single paned, CLEAR glass
  W1, W3, W4, W6, W8
Single door
  32” x 96” unit size
  RHIS or LHIS
  Square or Modern Handle (dummy set with magnet catch at top)
Double Door
  60” x 96” unit size
  Both Active INswing (small gap between door slabs)
  Square or Modern Handle (dummy set with magnet catch at top)

## Slide 6: Standard Swing – Insulated
Double Paned Glass
  System 25
    ESG 4/ 12 / ESG 4
  All glass options available
  1-point locking handle preferred hardware option
Comes with threshold
  Jamb Profile (matches the frame)
    Standard option
  Drop Sill (retractable seal)
    Available upon request

## Slide 7: Pivot
Equipped with pivot hinge
Available in all configurations
Slab width range: 30”- 60”
Slab height max: 108”

## Slide 8: Fixed
Maximum Sizes: 60” x 108”
Any configuration (W1, W2, W3, etc.)

## Slide 9: Pocket
Single Door
Double Door
Types of Pocket Hardware
  Hafele Slido Set (default, in-stock option)
  Hafele Hawa Porta (only in special cases)

## Slide 10: Pocket Hardware – Hafele Slido
In-stock pocket door hardware option
Available for single doors, double doors, and double doors with synchronization
Includes fitting set, soft closers, track, and frame set
Available in 4 sizes for each type of door system
  24-80
    24-28” wide, 0-80” tall
  24-96
    24-28” wide, 80.01-96” tall
  30-80
    30-40” wide, 0-80” tall
  30-96
    30-40” wide, 80.01-96” tall
Maximum Weight Limit – 80kg

## Slide 11: Pocket Hardware Cont. – Hafele Hawa Porta
Used for unique dimensions, something that does not fall within Slido parameters
Need to order from Hafele
Requires fitting set, aluminum track, soft closers
  Does not have a frame kit like Slido
Fits 0-63” wide, 0-106” tall
Maximum Weight Limit – 100kg

## Slide 12: Pocket Hardware Cont. – Emtek Recessed Pulls
We can pair Emtek recessed pulls with our pocket door applications
Sandcast Bronze Rustic Modern Rectangular Pocket Door Mortise Lock
  Keyed (2123)
  Passage (2124)
  Privacy (2125)
  Dummy (2126)
  Flat Black Bronze (FB)
  We can use our standard pulls with the understanding that they will not enter the pocket unless pocket is wide enough to accept them.

## Slide 13: Barn
Comes equipped with hardware from the factory
  Not compatible with outside hardware (Emtek, Hafele, etc.)
Rails are available in lengths up to ~120”
  Can connect multiple pieces to accommodate larger slabs
Maximum weight limit: 100kg

## Slide 14: Sliding
Comes equipped with track hardware from the factory
  Herkules 120 – comparable to Hafele in quality
Can be surface mounted on wall or mounted within the opening/ceiling
  Standard distance of slab from wall is 5mm
    Can be moved further if required (ex. larger baseboard on wall)
Max weight limit for sliding components: 120kg

## Slide 15: Variafold
Comes equipped with standard hardware from the factory
  Includes top and bottom track
    Bottom track recessed into floor
  Secured with flush bolts at bottom of the slab
  ~4mm (~1/8”) gap between panels when closed
Max size per panel: 36” x 96”
Max number of panels: 8 panels per direction

## Slide 16: Finishes
5 Standard Finishes
  RAL-7016 / ANTHRACITE GREY
  RAL-7022 / UMBRA GREY
  RAL-9003 / WHITE
  RAL-9005 / BLACK
  RAL-DB703 / LIGHT GREY
Other RAL options available upon request, but check with the Glenview Doors team before offering to a customer

## Slide 17: Hardware
Handles/Pulls
1-point magnetic lock, opened only with a handle

## Slide 18: Hardware Cont.
1-point magnetic lock with a patent insert (keyed)
1-point magnetic lock with a WC type insert (thumbturn)

## Slide 19: Glass
10 custom options
  Clear (standard)
  Privacy Options (addtl. $400 per panel)
    Satinato
    Bronze
    Graphite
    Satinato Graphite
    Dark Graphite
    Fluted
    Fluted Matte
    Estriado
    Wired